## Slide 1
SLR1.2 Memory and storage
Representing sound

## Slide 2
What is sound?

## Slide 3
How sound is sampled and stored in digital form
ADC
100100100100101001010011001
Digital
signal
Analogue
signal

## Slide 4
Sound wave
What affects the quality of a digitally converted sound wave?
Bit depth
(detail)
Sample rate
(speed)
+

## Slide 5
Sample rate and bit depth
The number of samples per second, measured in hertz (Hz).
A typical audio file is recorded at 44,100Hz – i.e., 44,100 samples per second.
3Hz sample rate
Sample rate: How often (frequency) the amplitude of a sound wave is recorded. The more often a sample is recorded, the smoother the playback will sound.
Notes: -

## Slide 6
Sample rate: How often (frequency) the amplitude of a sound wave is recorded. The more often a sample is recorded, the smoother the playback will sound.
The number of samples per second, measured in hertz (Hz).
A typical audio file is recorded at 44,100Hz – i.e., 44,100 samples per second.
Sample rate and bit depth
3Hz sample rate
6Hz sample rate
Notes: -

## Slide 7
Sample rate and bit depth
Bit depth: How many different gradations of amplitude can be represented in a digital waveform.
The amount of information stored with each sample, measured in bits.
Typically, CDs are 16-bit, meaning each sample takes up 2 bytes and can store one of 65,536 amplitudes.
2-bit depth
Notes: -

## Slide 8
Bit depth: How many different gradations of amplitude can be represented in a digital waveform.
The amount of information stored with each sample, measured in bits.
Typically, CDs are 16-bit, meaning each sample takes up 2 bytes and can store one of 65,536 amplitudes.
Sample rate and bit depth
2-bit depth
4-bit depth
Notes: -

## Slide 9
Sound file size = (Number of samples per second) x (Number of bits per sample) x (Length of sample in seconds)
Calculating sound sample sizes
Size of a sound file |  | 
Sample rate |  | Number of samples per second
Duration |  | Length of sample in seconds
Bit depth |  | Number of bits needed to store each sample
Notes: -

## Slide 10
Calculating sound sample sizes
Size of a sound file |  | 
Sample rate | 6 | Number of samples per second
Duration | 3 | Length of sample in seconds
Bit depth | 4 | Number of bits needed to store each sample
6 x 3 x 4 | = | 72 bits = 9 bytes
Sound file size = (Number of samples per second) x (Number of bits per sample) x (Length of sample in seconds)
Notes: -

## Slide 11
Sound file size: The total number of bits in a sound file. Calculated as: (Number of samples per second) x (Number of bits per sample) x (Length of sample in seconds).
Bit depth: The number of bits stored per sample. The higher the bit depth, the greater the quality of the sound and the larger the file size.
Sample rate: The number of samples stored per second. The higher the sample rate, the higher the quality of the sound, and the larger the file size.