## Slide 1
SLR1.3 Computer networks, connections and protocols
The use of IP and MAC addressing

## Slide 2
Every device on a network has a network interface card (NIC).
IP and MAC addressing

## Slide 3
Every device on a network has a network interface card (NIC)
Every NIC has a Media Access Control (MAC) address, which is used to route frames on a local area network (LAN).
IP and MAC addressing
00:0a:95:9d:68:16

## Slide 4
If the LAN is connected to a WAN such as the internet, a different addressing method is required.
IP addressing is used to route frames on a wide area network (WAN) – with a WAN, we refer to frames as packets.
IP and MAC addressing

## Slide 5
An IP (Internet Protocol) address is a unique number used to identify a host computer or node that communicates over the internet. There are currently two versions of IP in use today – IPv4 and IPv6.
IPv4
193 . 74 . 211 . 63
11000001 01001010 11010011 00111111
32 bits (4 bytes) in size
IPv4 format: Four numbers between 0 and 255 separated with periods.

## Slide 6
IPv4
128
64
32
16
8
4
2
1
128
64
32
16
8
4
2
1
128
64
32
16
8
4
2
1
128
64
32
16
8
4
2
1
0
1
1
0
1
1
1
1
0
1
0
1
1
1
1
0
0
0
1
1
1
0
0
0
0
1
1
0
1
0
1
1
107.56.94.111
107
56
94
111
IPv4 provides us with approximately 4 billion possible addresses from 000.000.000.000 – 255.255.255.255.
The actual number is slightly lower, as some addresses are reserved for special uses.

## Slide 7
IPv4
128
64
32
16
8
4
2
1
128
64
32
16
8
4
2
1
128
64
32
16
8
4
2
1
128
64
32
16
8
4
2
1
0
1
1
0
1
1
1
1
0
1
0
1
1
1
1
0
0
0
1
1
1
0
0
0
0
1
1
0
1
0
1
1
107.56.94.111
Network identifier (3 bytes): 107.56.94
Host identifier (1 byte): 111
An IPv4 address has two parts:
  Network identifier
  Host identifier

## Slide 8
Billions of devices
1992
1,000,000
The Internet of Things (IoT)

## Slide 9
Billions of devices
1992
1,000,000
2012
8.7 billion
The Internet of Things (IoT)

## Slide 10
Billions of devices
1992
1,000,000
2012
8.7 billion
2018
34.8 billion
The Internet of Things (IoT)

## Slide 11
Billions of devices
1992
1,000,000
2012
8.7 billion
2018
34.8 billion
2020
50.1 billion
The Internet of Things (IoT)

## Slide 12
49cd:c92d:dabb:469f:003c:4877:f44b:5441
0100100111001101 1100100100101101 1101101010111011 0100011010011111 0000000000111100 0100100001110111 1111010001001011 0101010001000001
128 bits (16 bytes) in size.
Approximately 340 trillion-trillion-trillion combinations
IPv6
IPv6 format: Eight groups of four 16-bit hex values separated by colons.

## Slide 13
MAC addressing is used to route frames on a local area network (LAN). Each MAC address is unique to every network interface card (e.g., 00:0a:95:9d:68:16).
IP addressing is used to route packets on a wide area network (WAN). There are two versions of IP addresses – IPv4 and IPv6.
IPv4:
  32 bits in size.
  Four numbers between 0 and 255 separated with periods (e.g., 69.89.31.212).
  A router has a unique WAN-facing IP address and a LAN-facing IP address – this enables a LAN device to have the same IP address as another device on a separate LAN.
  IPv4 is being replaced by IPv6 because unique static addresses are running out.
IPv6:
  128 bits in size.
  Eight groups of four 16-bit hex values separated by colons (e.g., 2001:0db8:85a3:0000:0000:8a2e:0370:7334).